# gTracker protocol (ver. 1)

Each message consists from header and body:
	L	T	Body
Size (in bytes)	1	1	Depends on message type

L – message length. This field is not counted in length.
T – message type
# Client messages
## Authenticate message.
	L	T	V	DeviceID
Value		0x41	1
Size (in bytes)	1	1	1	12 or 0

V – protocol version. Equal to 1.
If client connects first time DeviceID field shall have zero length. If client already has identity, it shall be passed in DeviceID field.
## Coordinate message
	L	T	Latitude degree	Latitude exponent	Longitude degree	Longitude exponent	Speed	Time Stamp	….
Value		0x43
Size (in bytes)	1	1	2	4	2	4	2	4
Size (in bytes)	1	1	18 ...

Body can contain several coordinates. Each coordinate consists from four fields: Latitude degree, Latitude exponent, Longitude degree, Longitude exponent, Speed and Time Stamp. Latitude and longitude are floats calculated by algorithm (described in Appendix A). Mantissa is a Latitude(Longitude) degree and exponent is a Latitude(Longitude) exponent. Speed is measured in km/h. Time Stamp field is a UTC time presented as count of seconds since Epoc (1 -Jan-1970).
## Heartbeat message
	L	T
Value		0x45
Size (in bytes)	1	1	0

Client shall send heartbeat message each minute. If both heartbeat and coordinate messages are absent within 2 minute interval, client will be dropped by server and track will be closed.
## SOS message
	L	T
Value		0x46
Size (in bytes)	1	1	0

This message can be send in case of emergency situation. The server can react somehow(e. g. sending SMS message).
## Start new track
	L	T	Track name
Value		0x47
Size (in bytes)	1	1	0..50

A new track with new name(if any) will be started right after this message arrival.
## Rename track
	L	T	Track name
Value		0x48
Size (in bytes)	1	1	0..50

Renames current track. If track name is empty (zero length), current track name is dropped.
# Server messages
## Authenticate response from server
	L	T	DeviceID	Reference
Value		0x42
Size (in bytes)	1	1	12	128

DeviceID field contains unique identity for connected client. The client shall store this identity and use it next time to connect (see Authenticate message). Reference is a null-terminated string Http reference to direct view of active track of the device. All trailing unused bytes are filled with zeros. This reference can be sent by eMail, SMS, etc.

## Track status
	L	T	Track name
Value		0x49
Size (in bytes)	1	1	50

Track new name.
## Error message
	L	T	Error code	Description
Value		0x44
Size (in bytes)	1	1	1	0...

Server may response with error. Possible error codes are described in Appendix B.
## Heartbeat message response
	L	T
Value		0x4a
Size (in bytes)	1	1	0

The server response to client Heartbeat message.
## Reconnect demand
	L	T	Host	Port
Value		0x4b
Size (in bytes)	1	1	128	4

The server demands client to reconnect to Host:Port, where Host is a null-terminated string and Port is a 4 byte integer. When client gets such message it MUST reconnects to given Host:Port.
# Appendix A
 TBD. Latitude/Longitude calculation algo.
# Appendix B
- ERROR_NOT_AUTH (0x01) – client not authenticated. Authenticate first.
- ERROR_WRONG_MSG (0x02) – wrong message. Message has wrong format for declared protocol version. Description field of Error Message contains message, which client sent to server.
- ERROR_FUCK_OFF (0x03) – client was disconnected after N attempts to send wrong data.
- ERROR_SERVER_UNAVAILABLE (0x04) – server not in working mode.
- ERROR_WRONG_DID(0x05) – wrong DeviceID
- ERROR_ALREADY_AUTH(0x06) – client with such DeviceID has already authenticated
- ERROR_TRACK_RENAME(0x07) – track rename failed
- ERROR_START_NEW_TRACK(0x08) – start new track failed
- ERROR_TRACK_NAME_TOO_LONG(0x09) – track name too long
- ERROR_TRACK_NOT_STARTED(0xA) – track is not started yet